## Slide 1
Obstacle Avoiding Car
Arduino Uno • Ultrasonic Sensor • Servo Motor • L298N • 2 DC Motors
Presented by
Rana Taha (0622) • Hamza (0624) • Hammad (0606) • Allyan (0616)

## Slide 2
Introduction
An obstacle-avoiding car is a robot that drives by itself and never needs a remote or driver.
It "sees" using an ultrasonic sensor, which works like a bat: it sends sound and measures the echo.
The Arduino Uno is the brain: it reads the distance and decides whether to go forward, reverse or turn.
The L298N driver is the muscle: it supplies enough current to the two DC motors that the Arduino pins cannot.
Objective: design a low-cost autonomous car that detects obstacles within 20 cm and finds a free path.

## Slide 3
Components Explained (1/2)
Arduino Uno
Microcontroller that runs our program. It reads the sensor, controls the servo and sends HIGH/LOW signals to the motor driver.
Ultrasonic Sensor
Has two parts: TRIG sends a sound pulse (40 kHz) and ECHO receives its reflection. The time taken tells us the distance.
Servo Motor
Rotates to an exact angle (0–180°). The sensor is mounted on it so the car can look right (15°), center (90°) and left (165°) without turning the body.

## Slide 4
Components Explained (2/2)
L298N Motor Driver
An H-bridge driver. IN1–IN4 inputs choose the direction of each motor; it supplies the higher current and voltage from the battery.
2 DC Motors
Left and right wheels. Both spinning forward = move ahead; spinning in opposite directions = the car turns on the spot.
Battery & Chassis
Battery powers the motors through the L298N; the chassis holds everything. All grounds (GND) must be joined together.

## Slide 5
How the Ultrasonic Sensor Measures Distance
Step 1
TRIG pin is set LOW for 2 µs, then HIGH for 10 µs to send a sound burst.
Step 2
pulseIn(ECHO, HIGH, 30000) measures how long ECHO stays HIGH (the round-trip time in µs). It waits at most 30 ms.
Step 3
Distance (cm) = duration × 0.034 / 2. Sound travels 0.034 cm per µs, and we divide by 2 because the sound goes to the object and back.
No echo?
If duration is 0 (nothing detected), the function returns 100 cm, meaning the path is clear.

## Slide 6
Pin Connections
Component | Pin | Arduino | Purpose
Ultrasonic | TRIG | D10 | Sends sound pulse
Ultrasonic | ECHO | D11 | Receives echo
L298N | IN1 | D4 | Motor A direction
L298N | IN2 | D5 | Motor A direction
L298N | IN3 | D6 | Motor B direction
L298N | IN4 | D7 | Motor B direction
Servo | Signal | D9 | Rotates the sensor
Servo/sensor get 5 V from Arduino; the L298N gets the battery. Join all GND together.

## Slide 7
Motor Logic Explained
Action | IN1 | IN2 | IN3 | IN4 | Result
Forward | HIGH | LOW | HIGH | LOW | Both motors forward
Backward | LOW | HIGH | LOW | HIGH | Both motors reverse
Turn Right | HIGH | LOW | LOW | HIGH | Motors opposite: spins right
Turn Left | LOW | HIGH | HIGH | LOW | Motors opposite: spins left
Stop | LOW | LOW | LOW | LOW | No power to motors
For each motor, HIGH/LOW = one direction, LOW/HIGH = the opposite direction, and LOW/LOW = stop. The code uses this in moveForward(), moveBackward(), turnRight(), turnLeft() and stopMotors().

## Slide 8
Working Principle (Step by Step)
1. Look ahead
Servo is at 90°. The car keeps measuring the front distance and prints it on the Serial Monitor.
2. Path clear
If the distance is 20 cm or more, moveForward() keeps the car running.
3. Obstacle found
If 0 < distance < 20 cm: stop for 300 ms, then reverse for 400 ms to make room.
4. Scan both sides
Servo turns to 15° (right) then 165° (left) and reads each distance.
5. Decide & turn
Servo returns to 90°. If right ≥ left the car turns right, otherwise left (500 ms), then goes forward again.

## Slide 9
Code Explained: Setup
#define
Names every pin (TRIG 10, ECHO 11, IN1–IN4 = 4–7, SERVO 9) and sets OBSTACLE_DISTANCE to 20 cm so it is easy to change.
Servo library
#include <Servo.h> and Servo servoMotor; create the servo object used to control angles.
setup()
Starts Serial at 9600 baud, sets TRIG and IN1–IN4 as OUTPUT, ECHO as INPUT, attaches the servo and centers it at 90°.
delay(2000)
Waits 2 seconds so the car is stable before it starts moving.

## Slide 10
Code Explained: Main Loop
Read distance
int distance = getDistance(); then print it with Serial.print.
If obstacle
Condition (distance > 0 && distance < 20): stopMotors → delay → moveBackward → stopMotors. The distance > 0 check ignores wrong readings.
Compare sides
distanceRight = lookRight(); distanceLeft = lookLeft(); servo is set back to 90°.
Choose turn
if (distanceRight >= distanceLeft) turnRight(); else turnLeft(); each turn lasts 500 ms and then the motors stop.
Else
If no obstacle, moveForward() runs. A 50 ms delay at the end keeps readings stable.

## Slide 11
Code Explained: Functions
getDistance()
Triggers the sensor, reads the echo time and returns the distance in cm (100 if timed out).
lookRight()
servoMotor.write(15), wait 500 ms for the servo to reach it, then returns getDistance().
lookLeft()
servoMotor.write(165), wait 500 ms, then returns getDistance().
Motor functions
Each uses digitalWrite on IN1–IN4 to set forward, backward, left, right or stop.

## Slide 12
Thank You